## Slide 1: Network service:-
A virtual private network (VPN)
VPN is a computer network that uses a public telecommunication such as the Internet to provide remote offices with secure access.
It aims to avoid an expensive system of owned or leased lines that can be used by only one organization.
It encapsulates data transfers between two or more networked devices which are not on the same private network.
so as to keep the transferred data private from other devices on one or more main local or wide area networks.
Virtual Private Networks reduce network costs because they avoid a need for many leased lines that individually connect to the Internet.
Users can exchange private data securely, making the expensive leased lines unnecessary.

## Slide 2: A virtual LAN:-
A virtual LAN, commonly known as a VLAN.
It is a group of hosts with a common set of requirements that communicate even though they were attached to the same broadcast domain or different physical location.
A VLAN has the same attributes as a physical LAN, but it allows for end stations to be grouped together even if they are not located on the same network switch.
Network reconfiguration can be done through software instead of physically transfer devices.
VLANs are created to provide the segmentation services usually provided by routers in LAN configurations.
VLANs address issues such as scalability, security, and network management.

## Slide 3
VLANs address issues such as scalability, security, and network management.
Wi-Fi :
Wi Fi is a trademark of the Wi-Fi Alliance.
A Wi-Fi enabled device connects to the Internet when within range of a wireless network connected to the Internet.
E.g. personal computer, video game console, smart phone or digital audio player.
The coverage of one or more (interconnected) access points — called hotspots.
Generally it includes an area the size of a few rooms but may be expanded to cover many square miles, depending on the number of access points with overlapping coverage.
In addition to private use in homes and offices, Wi-Fi can provide public access.

## Slide 4
This public access provided either free-of-charge or to subscribers to various commercial services.
Organizations and businesses - such as those running airports, hotels and restaurants - often provide free-use hotspots to attract or assist clients.
Wi-Fi certified and compliant devices are installed in many personal computers, video game consoles, MP3 players, smart phones, printers, digital cameras, and laptop computers.

## Slide 5: Remote sensing:
It is the small- or large-scale acquisition (to gain) of information of an object by using recording or real-time sensing device(s) that are wireless.
Remote sensing is the stand-off collection through the use of a variety of devices for gathering information on a given object or area.
Such as Earth observation or weather satellite data collection ,ocean and atmospheric observing , X-radiation (X-RAY) and space investigate are all examples of remote sensing.

## Slide 6
There are two main types of remote sensing:
    Passive remote sensing
    Active remote sensing
Passive remote sensing –
Passive sensors detect natural radiation that is emitted or reflected by the object or surrounding area being observed.
Examples of passive remote sensors include film photography, infrared, charge-coupled devices, and radiometers.
Active remote sensing –
In active remote sensing, it emits energy in order to scan objects and areas whereupon a sensor then detects and measures the radiation that is reflected or backscattered from the target.
RADAR is an example of active remote sensing where the time delay between emission and return is measured, establishing the location, height , speed and direction of an object.

## Slide 7: The Global Positioning System (GPS):
The Global Positioning System (GPS) is a space-based global navigation satellite system.
It provides reliable location and time information in all weather and at all times and anywhere on or near the Earth.
It is maintained by the United States government and is freely accessible by anyone with a GPS receiver.
GPS was created and realized by the U.S. Department of Defense (USDOD) and was originally run with 24 satellites.
It was established in 1973 to overcome the limitations of previous navigation systems.

## Slide 8
In addition to GPS other systems are in use or under development.
The Russian GLObal NAvigation Satellite System (GLONASS) was for use by the Russian military only until 2007.
There are also the planned Chinese Compass navigation system and Galileo positioning system of the European Union (EU).
A GPS receiver calculates its position by precisely timing the signals sent by GPS satellites high above the Earth.
Each satellite continually transmits messages that include

## Slide 9
* The time the message was transmitted
* Precise orbital information (the ephemeris)
* The general system health and rough orbits of all GPS satellites
(the almanac).
The current GPS consists of three major segments. These are the space segment (SS), a control segment (CS), and a user segment (US).
The U.S. Air Force develops, maintains, and operates the space and control segments.

## Slide 10
GPS satellites broadcast signals from space, and each GPS receiver uses these signals to calculate its three-dimensional location (latitude, longitude, and altitude) and the current time.
Fig shows the GPS

## Slide 11
General packet radio service (GPRS):
General packet radio service (GPRS) is a packet oriented mobile data service on the 2G and 3G cellular communication.
This system works for global system for mobile communications (GSM).
The service is available to users in over 200 countries worldwide.
GPRS was originally standardized by European Telecommunications Standards Institute (ETSI).

## Slide 12
It is now maintained by the 3rd Generation Partnership Project (3GPP).
In 2G systems, GPRS provides data rates of 56-114 kbit/second.
GPRS usage charging is based on volume of data, either as part of a bundle or on a pay as you use basis.
An example of a bundle is up to 5 GB per month for a fixed fee. Usage above the bundle cap is either charged for per megabyte or disallowed.
The pay as you use charging is typically per megabyte of traffic.

## Slide 13
GPRS extends the GSM circuit switched data capabilities and makes the following services possible:
* "Always on" internet access
* Multimedia messaging service (MMS)
* Push to talk over cellular (PoC/PTT)
* Instant messaging and presence—wireless village
* Internet applications for smart devices through wireless application protocol (WAP)
* Point-to-point (P2P) service: inter-networking with the Internet (IP)

## Slide 14
Fig shows the GPRS

## Slide 15
GSM (Global System for Mobile Communications):
GSM is the world's most popular standard for mobile telephony systems.
The GSM Association estimates that 80% of the global mobile market uses the standard.
GSM is used by over 1.5 billion people across more than 212 countries and territories.
This means that subscribers can use their phones throughout the world, enabled by international roaming arrangements between mobile network operators.

## Slide 16
GSM differs from its predecessor technologies in that both signaling and speech channels are digital.
Hence GSM is considered a second generation (2G) mobile phone system.
In GSM consumers have ability to roam and switch carriers without replacing phones.
And for network operators, who can choose equipment from many GSM equipment vendors.
GSM also established low-cost implementation of the short message service (SMS), also called text messaging.

## Slide 17
GSM is a cellular network, which means that mobile phones connect to it by searching for cells in the immediate vicinity.
There are five different cell sizes in a GSM network—macro, micro, pico, femto and umbrella cells.
The coverage area of each cell varies according to the implementation environment.
Macro cells can be regarded as cells where the base station antenna is installed on a mast or a building above average roof top level.

## Slide 18
Micro cells are cells whose antenna height is under average roof top level; they are typically used in urban areas.
Picocells are small cells whose coverage diameter is a few dozen metres; they are mainly used indoors.
Femtocells are cells designed for use in residential or small business environments and connect to the service provider’s network via a broadband internet connection.
Umbrella cells are used to cover shadowed regions of smaller cells and fill in gaps in coverage between those cells.

## Slide 19
The longest distance the GSM specification supports in practical use is 35 kilometres.
GSM networks operate in a number of different carrier frequency ranges with most 2G GSM networks operating in the 900 MHz or 1800 MHz bands.
Most 3G networks in Europe operate in the 2100 MHz frequency band.
One of the key features of GSM is the Subscriber Identity Module, commonly known as a SIM card.
The SIM is a detachable smart card containing the user's subscription information and phone book.

## Slide 20
Bluetooth
Bluetooth is a proprietary open wireless technology standard for exchanging data over short distances (using short wavelength radio transmissions).
It create personal area networks (PANs) with high levels of security.
Bluetooth was created by telecoms vendor Ericsson in 1994.
It was originally considered as a wireless alternative to RS-232 data cables.
It can connect several devices, overcoming problems of synchronization.

## Slide 21
Today Bluetooth is managed by the Bluetooth Special Interest Group.
Bluetooth uses a radio technology called frequency-hopping spread spectrum, which chops up the data being sent and transmits chunks of it on up to 79 bands (1 MHz each) in the range 2402-2480 MHz.
This range is in the globally unlicensed Industrial, e.g. Scientific and Medical (ISM) 2.4 GHz short-range radio frequency band.

## Slide 22
Bluetooth is a standard wire-replacement communications protocol primarily designed for low power consumption based on low-cost transceiver microchips in each device.
Because the devices use a radio (broadcast) communications system, they do not have to be in line of sight of each other.
Bluetooth is a packet-based protocol with a master-slave structure.

## Slide 23
One master may communicate with up to 7 slaves in a piconet; all devices share the master's clock.
A piconet is an ad-hoc computer network linking a wireless user group of devices using Bluetooth technology protocols.
The Bluetooth specifications are developed and licensed by the Bluetooth Special Interest Group (SIG).
The Bluetooth SIG consists of more than 13,000 companies in the areas of telecommunication, computing, networking, and consumer electronics.

## Slide 24
A videoconference or video conference (also known as a videoteleconference):
It is a set of interactive telecommunication technologies which allow two or more locations to interact via two-way video and audio transmissions simultaneously.
It has also been called 'visual collaboration' and is a type of groupware.
Videoconferencing differs from videophone calls in that it's designed to serve a conference rather than individuals.

## Slide 25
It is an intermediate form of videotelephony, first deployed commercially by AT&T during the early 1970s using their Picturephone technology.
Videoconferencing uses telecommunications of audio and video to bring people at different sites together for a meeting.
This can be as simple as a conversation between two people in private offices (point-to-point) or involve several sites (multi-point) with more than one person in large rooms at different sites.

## Slide 26
Besides the audio and visual transmission of meeting activities, videoconferencing can be used to share documents, computer-displayed information, and whiteboards.
Voice over Internet Protocol (Voice over IP, VoIP):
It is one of a family of internet technologies, communication protocols, and transmission technologies for delivery of voice communications and multimedia sessions over Internet Protocol (IP) networks, such as the Internet.

## Slide 27
It is also called as IP telephony, Internet telephony, voice over broadband (VoBB), broadband telephony, and broadband phone.
Internet telephony refers to communications services — voice, fax, SMS, and/or voice-messaging applications — that are transported via the Internet, rather than the public switched telephone network (PSTN).
The steps involved in originating a VoIP telephone call are signaling and media channel setup, digitization of the analog voice signal, encoding, packetization, and transmission as Internet Protocol (IP) packets over a packet-switched network.

## Slide 28
On the receiving side, similar steps (usually in the reverse order) such as reception of the IP packets, decoding of the packets and digital-to-analog conversion reproduce the original voice stream.
Use of Skype:
Skype is a proprietary Voice over IP service and software application.
Skype was first released in 2003 written by Estonian developers Ahti Heinla, Priit Kasesalu, and Jaan Tallinn, who had also originally developed Kazaa.

## Slide 29
The service allows users to communicate with peers by voice using a microphone, video by using a webcam, and instant messaging over the Internet.
Calls to other users within the Skype service are free of charge, while calls to landline telephones and mobile phones are charged via a debit-based user account system.
Skype has also become popular for its additional features, including filetransfer and videoconferencing.

## Slide 30
The network is operated by Microsoft, which has its Skype division headquarters in Luxembourg.
Unlike most other VoIP services, Skype is a hybrid peer-to-peer and client–server system.
Registered users of Skype are identified by a unique Skype Name, and may be listed in the Skype directory.
Skype allows these registered users to communicate through both instant messaging and voice chat.

## Slide 31
Skype supports conference calls up to 25 people at a time.
Skype also supports video chat, including screen sharing, between two people for free.
Skype does not provide the ability to call emergency numbers. E.g. 911 in North America.
Skype runs on a number of platforms including Microsoft Windows (XP, Vista, 7, 8), OS X (10.5.8 or newer), Linux (Ubuntu and others), Android, BlackBerry 10, iOS, Symbian and Windows Phone.

## Slide 32
Skype also offers a Skype Wi-Fi Phone, which is a wireless mobile phone that allows users to make Skype calls, using a wireless Internet connection.
Skype uses a proprietary Internet telephony (VoIP) network called the Skype protocol.
Skype is claimed to be a secure communication; encryption cannot be disabled, and is invisible to the user.

## Slide 33
Wi-Fi :

## Slide 34
virtual private network (VPN)